Short Answer Questions:
1. What is the difference between network layer and transport layer since they are both carrying logical communications?
  Network layer is logical communication between hosts while transport layer is logical communication between processes
2. What is the difference between network layer and data link layer?
  Data link layer is physical while network layer is logical
3. Please give three differences between TCP and UDP.
  TCP provides flow control, congestion control, and reliable in order byte stream
4. What is multiplexing at sender? What is de-multiplexing at receiver?
Multiplexing at sender handles data from multiple sockets, and adds a transport layer	header used for demultiplexing at reciever to deliver into the correct socket
1. . What is the difference between UDP socket and TCP socket?
  TCP socket requires source and destination IP, while UDP only requires destination IP
2. What is the usual size of UDP header?
  8 bytes
3. What is the usual size of IPv4 header?.
  20 bytes
4. What is the purpose of UDP checksum?
  To detect errors
5. What is the problem and solution in rdt 2.0, rdt 2.1, and rdt 3?
  1.0: assume no errors or packet loss occur solution: 2.0
  2.0: bits may be flipped, introduce a checksum, how to recover from these errors? ACK and NAK- may be corrupted
  2.1: send one packet and wait for reciever response (stop and wait)
  2.2: get rid of NAK, include sequence number in ACK – duplicate ACK results in retransmission
  3.0: The channel can also lose packets (ACK's, Data), senders waits reasonable amount of time for ACK, if not recieved in time, retransmit
6. For non-pipelined protocols, why does sequence number surface (0, 1) suffice? .
  0 and 1 will alternate for each packet recieved- if a 0 is recieved after another 0, or a 1 is recieved after another 1, retransmit
7. What is the difference between stop-and-wait protocols and pipelined protocols?
  Pipelined protocols allow for transmission of more packets concurrently
8. What is called cumulative ACK?
  It tells the sender that you have recieved packets up to a certain point
9. Why does Selective Repeat have the dilemma when seq #’s: 0, 1, 2, 3 and window size=3?
  Duplicate data can be accepted as new
10. For k-bit sequence number, what is the window size for GBN and Selective Repeat respectively?
  GBN – 2k, largest sequence number – 2k -1
  Selective repeat – 2k-1 , largest sequence number- 2k-1 -1
11. Give at least five features of TCP which UDP doesn’t have.
  Flow control, congestion control, in order byte stream, 3 way handshake,
12. What is called TCP fast retransmit?
  Retransmit on Tiple duplicate ACK, as segment is likely lost
13. Give me two indicators of a data loss.
  Time out, duplicate ACK
14. What is the definition for sequence number and acknowledgement number respectively in TCP?
 Sequence number: byte stream "number" of first byte in segment's data
ACK number: squence number of next byte expected from other side
1. Among the packet headers, which layer header contains port number? Which layer header contains IP address? Which layer header contains physical address?
  Network layer, Link layer
2. What is the major difference between TCP flow control and congestion control?
  Flow control: sender will not overwhelm reciever
  Congestion Control – too many sources sending too much data too fast
3. How does the receiver “advertises” free buffer space (amount recorded by rwnd) in TCP header?
4. Why do we need preamble in packet format?
  To synchronize reciever and sender clock rates – 7 bytes of (10101010) followed by one byte of (10101011)
5. Give me three costs of congestions.
  No retransmission with infinte buffer, retransmission of timed out packet with finite buffer, any upstream transmission capacity used for dropped packet was wasted
6. Why does TCP have faireness?
  Allows for parallel connections
7. What is called “longest prefix matching”?
  When looking for forwarding table entry for given destination address, use longest prefix that matches destination address
8. IP address: What is subset part and host part?
  Subnet part – high order bits
  host part – low order bits
9. CIDR: What does “x” mean in “a.b.c.d/x”?
x is # of bits in subnet portion of address
1. NAT: why can the internal computers use private addresses like “10.0.0.1”? .
  The NAT router will translate the private address to a public one
2. In distance vector algorithm, give me two conditions that may cause the router to re-compute the distance vector estimates?
  If it's neighbor sends an updated estimate
  If there is a change in a local link
3. What is the difference between inter-AS and intra-As protocols?
  Intra-AS is used by routers in the same AS
  Inter-AS is used to forward data outside of ASI and propogate reachability to other routers in the same ASI
4. What is the functionality of inter-AS protocol?
5. What is called “hot potato routing”?
  Sned packets towards closest of 2 routers
6. What is the difference between eBGP and iBGP?
  eBGP : obtain subnet reachability information from neighboring AS's
  iBGP: propagate reachability information to all ASI routers
7. What is the difference between TDMA and FDMA?
  TDMA: Time divison multiple access – each station gets a fixed length slot, unused slots go idle
  FDMA- frequency division multiple access – channel spectrum divided into frequency bands, each station assigned fixed frequency band, unused bands go idle
8. List two common drawbacks for “taking turns” MAC protocols.
  Token overhead
  Single point of failure

True or False Questions:
1. Multiplexing occurs at receiver and de-multiplexing occurs at sender.
  False, multiplexing occurs at sender, de-multiplexing occurs at reciever
2. UDP socket is identified by 4-tuple: source IP, source port number, destination IP and destination port number.
  False, TCP is identified by the 4-tuple
3. Checksum can be used to detect transmission error 100% correct.
  False, different packets may match the same checksum
4. rdt 3.0 is a pipelined protocol as it is much better than rdt 2.0.
  False, rdt3.0 uses stop and wait protocol
5. Stop-and-wait protocols are better than pipelined protocols regarding performance and network utilization.
  False, pipelined protocols have better preformance and utilization
6. Selective Repeat utilizes cumulative ACK.
  True
7. GBN has buffers at the receiver’s side.
  False, Selective repeat has buffers at recievers side
8. Network layer protocols are only for routers.
  False, network layer protocols are used inevery host and routers
9. Forwarding and routing are totally independent.
  False, forwarding and routing are interplayed together
10. Forwarding table uses individual IP addresses as indexes for each entry.
11. Internet is based on datagram network, which is reliable.
12. IP address is flat.
  False, MAC address is flat
13. Like TCP and UDP, ICMP is a transport layer protocol.
  False, ICMP is a network layer protocol
14. In tunneling technique, IPv4 is carried as payload of IPv6 packet.
  False, Ipv6 is carried as a payload in Ipv4 packet
15. Link state algorithm is appropriate for use in large-scale networks.
  False, link state is good for small networks as it requires a complete topology
16. For broadcasting, in-network duplication is better than source duplication..
  True
17. What is called reverse path forwarding (RPF)-based controlled flooding?
  Only forward packet if it arrived on shortest path between node and source
18. Data link layer studies logical communication between remote hosts or processes.
  False, transport layer and network layer studies this
19. With CSMA, there is no possibility to have collisions.
  False, collisions may occur due to propagation delay
20. MAC address is hierarchical.
  False, IP address is hierarchical
21. MAC address is portable.
  True
22. What is the difference between switch and router?
  Switches are link layer devices that use flooding and MAC addresses
  routers are network layer devices that rely on forwarding tables and IP addresses